IN MY AWESOME QGIS PROJECT…

THE CURRENT MAP CANVAS IS: / OR FOR A SPECIFIED LOCATION AND SCALE (5000):	BUT YOU CAN CAN GET IT AT A SPECIFIED SCALE (1:10000): / OR AT THE PROJECT EXTENT

in the global variable are loaded general informations about the current project
project	The project object instance		{{ globals.project }}
canvas	The map canvas object instance	from where you can access all QgsMapCanvas API methods:	{{ globals.mapCanvas }} / {{ globals.mapCanvas.layerCount() }} / {{ globals.mapCanvas.scale() }}
extent	The current map canvas extent		{{ globals.extent }}
vars	A dictionary with the current global variables		{{ globals.vars }}

The map images have to be inserted with image filter using a image placeholder. The image tag have to be placed in name slot under option tab in image properties dialog:

image	A jinja2 filter to insert a map imagewith the following parameters: / dpi A integer number specifying the output resolution of the image (default = 200) / box A extent object that specify the map context of the image / center A point object that specify the center of the map context of the image. To be used in conjunction with scale_denominator / scale_denominator A number specifiing the scale_denominator of the output image, for example 5000 for 1:5000 / theme A string indicating a map canvas theme of representation / around_border A floating number representing the amount of a void border around the output image (default = 0.1)	The image dimension on the paper is defined by a image pleceholder that will be replaced during document rendering. / The tag has to be placed in name parameter under options slot of image properties / the filter can be used with many parameters, even comma separated, in conjuntion each other. / globals|image() / globals|image(scale_denominator=20000) / globals|image(dpi=600, scale_denominator=20000)

Template tags have to be inserted in odt document as visual field: in LibreOffice Writer from the menu Insert > Fields > Other... (or just press Ctrl+F2), then click on the Functions tab and select Input field. Click Insert. A dialog will appear where you can insert the template tags following general jinja2 rules. Avoid inserting tags as regular text, this is not detected by template engine and may result in encoding error.

For example you can get the project variables list with the following instructions:

and this is the result:

{% for key,value in globals.vars.items() %} {{ key|replace("\n","") }}:
{{ value|replace("\n","")+"\n" }}{% endfor %}